Our 8-stage LSFR consists of 8 Registers, from right to left respectively, S7 to S0, with each latch connected to the next registers’ data input.
 XOR gates connected to the outputs of Registers S7, s6, s5, s2, s1 and s0 to calculate the feedback value.

Starting from S0 ⊕ S1, the result is sent only to the next XOR gate which is connected to the next register (S2) and then the result of S2 ⊕ S1 ⊕ S0 is sent to XOR connected to S5 and so on until it reaches S7.

The output sequence is the output of the latch of Register S0.

We used the Registers’ Reset and Chip enable functionality as control signals to be able to reset and re-initialize the LSFR, and to have idle cycles.

Register S7 receives the initial value the first 8 cycles, and afterwards it receives the feedback value. We implemented two ways to handle this, both of which can be found on our GitHub Repository: https://github.com/Ary-x86/EssCS-2024---Group-70-Mini-Project---Handout-2

The simpler one uses a multiplexer and a manual select control signal, which should be toggled manually after each Reset. This is the circuit we handed in, since it reduces the gate equivalence value, trading it for 1 control signal (SELECT)

The more complex circuit called “D-70-submission1_AUTOMATIC.dig” can be foud on our GitHub. This circuit uses a counter and a comparator to automatically generate the appropriate select signal. The functionality is the same, only with one control signal less. It works with the RESET and CHIP ENABLE control signals, handles the counter’s bit-overflow with a Register and some combinational logic. More details can be found on the github repo.